## Slide 1
FEL-1 Techno-Economic Assessment of a New Technology Route for Production of Propylene by Bromination of Propane
Michael Xing, Yunus Ross, Selina Liu
06/07/22

## Slide 2: Process Design Overview
Background:
Current global propylene
market value: $3.7 billion
$5.7 billion by 2030 with a 4.5% compound annual growth rate
Chemical Species | Price
Polymer-Grade Propylene (C3H6) | $900/MT
Pure Propane (C3H8) | $200/MT
Pure Hydrogen (H2) | $1400/MT
Bromine (Br2) | $3000/MT
CO2 Charge | $75/MT
Fuel | $4.25 /GJ
Objective:
New chemical routes to produce propylene from bromination of propane
Produce 100 kta of 99.5% purity Propylene

## Slide 3: Simplified Process Flow Diagram (Without Heat Exchangers)
NPV: $18 MM; Total Capital Cost: $169 MM; Total Operating Cost: $31 MM/yr
Sub Plant 1
Sub Plant 2
Sub Plant 3

## Slide 4: PFR Reactor Variables Determination
Sub-plant 1, first reactor: Propane:Bromine = 3:1, Reactor Temperature = 350°C
Sub-plant 1, second reactor: Hydrogen:Dibromopropane = 3:1, Conversion = 0.92
Sub-plant 2 reactor: N-bromopropane conversion = 0.88
Reactor Volume Vs. Conversion
Selectivity Vs. Conversion

## Slide 5: Electrochemical Plant Design
To recycle the waste HBr back to Br2 and H2 , an electrochemical plant was designed.
In designing electrochemical plant, the primary design variables were the voltage of the reactor and the operating temperature.
Reactor Capital Cost Vs Voltage
Final Operating Conditions :
Temperature: 75 °C
Voltage: 1.25 V
Power Usage: 2.6 MW
Operating Cost: $8 MM/yr
Capital Cost: $26 MM
1.25V
$26 MM

## Slide 6: Heat System Design
Image Source: sciencedirect.com
This design requires high temperature for reactions and separations, so the process will be heat intensive
To get the best possible ratio on capital cost to operating cost, the heat exchangers and reboilers of the distillation column were also integrated in to overall heat exchanger system
System Type | dT (°C) | dH (MW)
Heating | 381 | 67
Cooling | -374 | -61
Final Heating Table:
Final Heating Values:
Total Power Exchanged: 32 MW
Energy Consumption: 32.8 MJ/kg of propylene product produced
Total Carbon footprint: 1.4 CO2 kta of per kta of propylene.

## Slide 7: Economic Analysis Model
Category | Value
Total Capital Cost, TCI | $169MM
Revenue, R | $65 MM/yr
Operating Cost, OpX | $31MM/yr
HYSYS ISBL ~ $62 MM
Including: 3 PFR Reactor
1 Electrochemical Reactor
6 Distillation Column
4 Furnace
3 Heater
1 Cooler
Assumption: 2-year Construction, 13-year Plant Life
Start-Up Cost = 10% FCI, Working Capital = 10% FCI, Salvage = 5% FCI
Tax Rate =27%
Annual Interest Rate = 10%
Depreciation: 10-year linear schedule

## Slide 8: Capital Cost And Operating Cost Attribution
Distillation columns and reactors each takes ~44% of total CapX
Electrochemical reactor takes 41% total CapX ～$26MM
Distillation columns has the largest operating cost ~ 49%
Distillation Column | Pressure (bar) | No. Stages & Feed Stage | Height (m) | Reboiler Duty (MW) | Condenser Duty (MW) | Reflux Ratio | Material
1 | 30 | 20 & 4 | 14 | 5.3 | 1.2 | 2 | Solid Titanium*
2 | 30 | 55 & 19 | 34 | 6 | 0.4 | 8.7 | Solid Titanium*
3 | 30 | 52 & 20 | 31 | 3.4 | 1.2 | 2.3 | Solid Titanium*
4 | 30 | 30 & 10 | 20 | 0.25 | 0.3 | 5 | Solid Titanium*
5 | 20 | 40 & 19 | 26 | 6 | 0.4 | 21 | Solid Titanium*
6 | 20 | 60 & 22 | 37 | 6.1 | 0.4 | 3.2 | Solid Titanium*

## Slide 9: NPV Optimization
* Optimal Values for Design Variables: s = 0.87 (at MR =3, T = 350°C)
Profitability Metric | Value
Net Present Value, NPV | $18MM
NPV% | 0.69%
IRR | 12.04%

## Slide 10: Sensitivity Analysis
Analysis based on ±15% price variation
Fluctuation in propylene selling price has the greatest impact on profitability

## Slide 11: Process Safety
Due to the existence of different corrosive materials such as Br2, HBr and H2 non conventional building materials may be needed
Monel
Stainless Steel
Image Sources in order Left:thoughtco.com, Middle: made-in-china.com, Right:tantec-group.com
Tantalum
Br2 H2
Br2 HBr
However Tantalum is 20x the price of Titanium
For this process to be successful, a more detailed materials safety analysis is required
High T (?)

## Slide 12: Summary
Results
TCI: $169MM, NPV: $18MM, NPV%: 0.69%, IRR: 12.04%
The energy consumed by the process: 32.8MJ/kg propylene
The CO2 produced by the process: 1.4kg CO2/kg propylene
Distillation columns attributes the most to CapX and OpX; electrochemical reactor following in the second place has CapX of $26MM
Conclusion
The design will make profits, but the amount may be negligible; whether the design is worth operating is still debatable and will depend on the future work conducted
Future Work
A more detailed material safety analysis is required
More analysis for the viability of the electrochemical reactor is suggested

## Slide 13
Thank You!

## Slide 14: Reaction Chemistry
Reaction | Standard Potential (V)
Br2+2e- ⇌ 2Br- | 1.087
2H-+2e- ⇌ H2 | 0
Catalyst | Price ($/kg) | Diameter (mm) | Length (mm) | Surface Area (m2/gram) | Particle Density (kg/liter) | Void Fraction (%)
Hydrogenation | 140 | 10 | 20 | 100 | 0.88 | 50
Dehydrobromination | 10 | 15 | 25 | 100 | 0.5 | 50

## Slide 15: Detailed Process Flow Diagram (Including Heat Exchangers)

## Slide 16: Level 2&3 Flow Diagram and Balances

## Slide 17: Sub-plant 1 & 2 Variable Values Determination

## Slide 18: Electrochemical Plant Calculations
Experimental Data:
CapX=I/(A[V]*e[V])*10000
OpX=I*V*Cost of Energy
Where I is the current, A is the current density, and e is the faradaic efficiency.
The plant separates water using dehumidifying salts such as sodium sulfate

## Slide 19: CFA Spreadsheet

## Slide 20: Heat Trim
HeatX | dH | dT | A (m2) | A (ft2) | Price | Water Cos/ Heat Transfer Fluid Cost | Total Cost
1 | 5,000 | 120 | 278 | 2,990 | $2,645,886 | N/A | N/A
2 | 5,450 | 80 | 454 | 4,889 | $3,642,149 | N/A | N/A
3 | 1,354 | 100 | 90 | 971 | $1,273,962 | N/A | N/A
4 | 1,354 | 100 | 90 | 971 | $1,273,962 | N/A | N/A
5* | 12,090 | 15 | 5,373 | 57,838 | $18,147,893 | N/A | N/A
6 | 3,407 | 120 | 189 | 2,037 | $2,061,971 | N/A | N/A
7 | 2,334 | 15 | 1,037 | 11,166 | $6,230,382 | N/A | N/A
8 | 3,246 | 25 | 866 | 9,317 | $5,538,906 | N/A | N/A